## Slide 1
FlowShadow: Keeping Update Consistency in Software-based OpenFlow Switches
Yi Wang, Dongzhe Tai, Ting Zhang, Bin Liu
† Tsinghua University
‡ Huawei Future Network Theory Lab, Hong Kong

## Slide 2: — Outline
1. Introduction
2. Motivation
3. FlowShadow Framework
4. Evaluation Results
5. Conclusion
Introduction
Framework
Results
Conclusion
Motivation

## Slide 3: —— Outline
1. Introduction
2. Motivation
3. FlowShadow Framework
4. Evaluation Results
5. Conclusion
Introduction
Framework
Results
Conclusion
Motivation

## Slide 4: Background
SDN is a new architecture：
  Central Control plane
  Efficient Management
  High Network utilization: from 30% to 90%
  ……
Introduction
Framework
Results
Conclusion
Motivation
ROA NBI

## Slide 5: Background
SDN Hardware Switch
  No ASIC designed for SDN
  Why: SDN iterated too fast to develop a ASIC
Introduction
Framework
Results
Conclusion
Motivation
Industry
Many Core
Commercial
ASIC
FPGA/NP
Academia
TI&Stanford

## Slide 6: — Outline
1. Introduction
2. Motivation
3. FlowShadow Framework
4. Evaluation Results
5. Conclusion
Introduction
Framework
Results
Conclusion
Motivation

## Slide 7: Motivation
Software-based SDN switch
  Two data plane:
    Slow Path with rule tables: wildcard match
    Fast Path with Microflows: exact match
  Microflows in Fast Path is specific flows of rules in Slow Path
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 8: Motivation
  Cache: a practical way to improve the performance of software-based OpenFlow switches
Open vSwitch: The most widely used software OpenFlow switches. Points of concern:
  Increase the throughput of switch
  Keep update consistency
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 9: Motivation
Cache Update Consistency
  Definition: A rule in OpenFlow table is changed or removed, the corresponding cache entry should be removed immediately.
  The modification of a rule  Modifying the Microflows
  One example…
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 10: Motivation
Update consistency
OpenFlow Table
Output:1
166.111.*.*
.
.
.
Output:2
59.66.*.*
Action
Dst IP
Cache
.
.
.
166.111.8.28
Output:1
59.66.131.51
Output:2
Dst IP
Action
P3
P2
P1
Host
IP：166.111.8.28
Port 3 Input queue
Dst ip=166.111.8.28
num=x+2
Dst ip=166.111.8.28
num=x+1
Dst ip=166.111.8.28
num=x
Succeed
Failed
Change Host’s Position
Update rule’s Action Output:1 to Output 2
Output:2
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 11: Motivation
The design goal of this paper
  Improve the throughput of OpenFlow switches
  Keep cache update consistency in OpenFlow switches
FlowShadow achieve the above objectives by adding additional data structure
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 12: FlowShadow Framework
FlowShadow is a framework for the Fast Path
  Applied a new mechanism to keep update consistency
  a signature is generated from the fields, signature is hashed into a bucket
  The signature is compared with all the signatures stored in this bucket
    Find，forward the packet according to the action
    Not find，search in openflow table
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 13: FlowShadow Framework
FlowShadow applies Action Table and Cookie Table to keep update consistency
  Action table final status of all the final cascade action: valid or invalid.
  Cookie table record the relationship between rules and the actions depend on this rule.
Resolve the conflict between the actions have the same value.
  Add a new column in Action Table: TimeStamp
  TimeStamp is used to mark whether the Microflows’ corresponding rules are modified.
  Action table record each rule’s final cascade action.
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 14: FlowShadow Framework
A single rule table example:
  1. Updating the Rule M in flow table;
  2. Resetting the TimeStamp of the Action(s) of Rule M;
  3. When the packet of a microflow that is one of the Rule M is arrived, looking up the Microflow table. Before executing the action, FlowShadow checks the TimeStamp.
    If the Microflow’s TimeStamp is less than the Action’s TimeStamp  Forwarding the packet to slow path;
    otherwise, excuting the action.
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 15: — Outline
1. Introduction
2. Motivation
3. FlowShadow Framework
4. Evaluation Results
5. Conclusion
Introduction
Framework
Results
Conclusion
Motivation

## Slide 16: Experience Setup
Open vSwitch (release version 2.1.2)
Linux Operating System in the version 2.6.41.9- 1.fc15.x86 64.
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 17: Experience Setup
Trace: Download form CAIDA
  captured from 3 different network: campuse, enterprise and backbone
  Each sustains 5 mins
Flow Table: two real table
  IP prefix table download from RIPE contains 388344 entries
  ACL contains 752 rules
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 18: Evaluation Results
Cache hit rate
  Cache size = Bucket number * bucket size，bucket size can be 1,2 or 4
  Result:
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 19: Evaluation Results
Look up speed in different update rate
  One flow table
  10% rules are modified per second
  Result:
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 20: Evaluation Results
Scalability
  Cache size =100k
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 21: Evaluation Results
The System performance
  1 flow table and cache size=100K, OpenMP API
  commodity PC that contains 2 CPUs (total 24 physical threads)
  system achieves the highest performance with 24 work threads
Introduction
Analysis
Results
Conclusion
Algorithm
Notes:     Direct replacement strategy when the bucket size is 1
    PLRU strategy when the bucket size is 2 or 4
    The performance of the direct replacement strategy is close to PLRU
    FlowShadow with 100K entries in the cache achieves 94.22% and 95.9% cache hit rates with the direct replacement strategy.

## Slide 22: Evaluation Results
The System performance
  24 threads
  Different cache size and flow table number
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 23: — Outline
1. Introduction
2. Motivation
3. FlowShadow Framework
4. Evaluation Results
5. Conclusion
Introduction
Framework
Results
Conclusion
Motivation

## Slide 24: Conclusion
Software-based flow table is a practical method to implement SDN, but need to be further improved:
  The throughput of the switch
  Update consistency
We proposed FlowShadow and three approach to guarantee update consistency in this paper
  Strictly guarantee update consistency
  FlowShadow has better update performance and good scalability under different update speeds and different numbers of flow tables
  The throughput of FlowShadow can be 3.4X of original OVS
Introduction
Analysis
Results
Conclusion
Algorithm

## Slide 25
Thanks
Q & A