## Slide 1
RuleTris: Minimizing Rule Update Latency for TCAM-based SDN Switches
小组成员：张豪、崔浩、钟春蒙、张苏坤

## Slide 2
Motivation
01
TCAM流表更新瓶颈
(Ternary Content-Addressable Memory)
  10s to 100s of rule operations per second
现有控制器生成膨胀的流表更新
不必要的优先级更新
  大规模的TCAM内部移动
Ultimate Goal:最小化TCAM更新操作以加速更新
Only update the “diff”

## Slide 3
Motivating Example
01
Update schedule with priority clue
  1 rule adds + 4 rule moves
Update schedule with dependency graph
  1 rule adds + 2 rule moves
Such redundant moves contribute over 95% in average!

## Slide 4
Key Insight
03
Dependency Graph (DAG) provides two optimality guarantees:
Minimum size flow table
Minimum number of TCAM moves for table update
1.How to efficiently generate DAG?
  O(n2) algorithm to obtain DAG from scratch
  Usually takes minutes for a thousand rules
2.How to efficiently optimize updates with DAG?
  Slow processor, limited memory on switches

## Slide 5
RuleTris Architecture
02
Front-end in controller
  An incremental SDN policy compiler that preserves DAG
Back-end in switch firmware
  Redundancy Eliminator, Update Scheduler…
F/B Interface
  Flow table + DAG

## Slide 6
How to efficiently generate DAG?
03
Our approach
  Track DAG along with flow table compilation
  （跟踪DAG以及流表编译）
  Linear additional time complexity!
  Will provide background on composition compiler first !

## Slide 7
Background: Flow Table Composition
03
Combine multiple flow tables into one functional equivalent flow table
Two operators: parallel, sequential
Parallel of Monitor and Route
Sequential of LB and Route

## Slide 8
Background: Composition Compiler without DAG
03
Compile multiple flow tables into a single flow table
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
Priority
Match
Action
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30
 count, fwd(1)

## Slide 9
Background: Composition Compiler without DAG
03
Compile multiple flow tables into a single flow table
9. srcip=1.0.0.0/24  count
0. *  drop
Monitor
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop
Router
Priority
Match
Action
16. srcip=1.0.0.0/24, dstip=2.0.0.0/30  count, fwd(1)
9. srcip=1.0.0.0/24  count
7. dstip=2.0.0.0/30  fwd(1)
0. *  drop

## Slide 10
RuleTris Composition Compiler
03
A generic composition compiler which features
DAG preservation during composition
  Parallel
  Sequential
  prioity
Efficient incremental compilation

## Slide 11
DAG preservation for Parallel Composition
04-1
Infer dependency relations via graph cross product
Then eliminate those with empty match

## Slide 12
DAG preservation for Parallel Composition
04-1
Special treatment for redundant rules:
not delete but indexes with the nested graph data structure

## Slide 13
DAG Preservation for Sequential Composition
04-2
Also eliminate empty and redundant rules

## Slide 14
DAG Preservation for priority Composition
04-3
通过找mega dependency 来将两个表缝合起来。

## Slide 15
DAG Preservation for priority Composition
04-3
找T2中的每个sink结点到T1种的每个source结点，作为试验边。如A->Z,B->Z;
对于每个试验边r2->r1，检查两个规则r1和r2的匹配是否重叠。如果是，则将边r2->r1放入结果DAG中。 否则，递归地生成试验边：
看每个r2结点的前任r3，如A的前任C,D，如果，r3比r2更通配，且与r1重叠，将r3->r1加入DAG中并设为试验边。（C->Z, D->Z）；
看r1的后任结点r4，如X,Y。如果r1不必r4严格通配。（ ）。则把r2->r4加入试验边。
递归验证每条试验边。

## Slide 16
Back-end OPTIMIZER
05
Update Scheduler
  Given delta flow table and delta DAG
  Calculate the update schedule with minimum number of TCAM moves
Redundancy Eliminator
CacheFlow Manager

## Slide 17
Back-end OPTIMIZER
05
Rule Insertion
  Step 1: Find TCAM location range for the inserted rule(eg:d & e)
  Step 2: Find nearest upper slot and lower slot
  Step 3: Search for shortest moving chain upwards and downwards
  Step 4: Use the shorter path for actual update
Shortest Moving Chain Searching
  Dynamic programming

## Slide 18
Implementation
06
RuleTris front-end
  Stand-alone composition compiler
  5K lines of Java code
  Interface with open-source Ryu controller
RuleTris back-end
  Implemented in firmware of an FPGA-based hardware switch, ONetSwitch
  3K lines of C code
Front-end/back-end communication
  Extension to OpenFlow protocol for carrying DAG and DAG updates

## Slide 19
Evaluation Results
07
Compare with two priority based approaches
  Baseline
  CoVisor [NSDI 2015]: incremental update
Experiment 1: Parallel composition
Rule update overhead of L3-L4 monitoring + L3 router.

## Slide 20
Evaluation Results
07
Compare with two priority based approaches
  Baseline
  CoVisor [NSDI 2015]: incremental update
Experiment 2: Sequential composition
Rule update overhead of L3-L4 NAT > L3 router.

## Slide 21
Evaluation Results
07
对于每规则更新延迟，RuleTris的中位数<12毫秒且90%的结果小于<15毫秒。
甚至超过在同一硬件交换机上部署的CoVisor近20倍。
RuleTris is a novel SDN policy update optimization framework
It minimizes rule update latency for TCAM-based SDN switches